## Slide 1: Velocys Pilot Plant Reactors for Catalyst Discharge Development
Orientation and overview

## Slide 2: Catalyst Discharge Development
Reactors
Velocys Pilot Plant Reactor 2 (VPP2)
Velocys Pilot Plant Reactor 4D (VPP4D)
-reactor currently operating and soon to be ready for discharge development work
-’core’ of reactor encased in pressure containment shell (PCS)
-reactor with hard to discharge catalyst
-possibly representative of ‘off condition’ reactor
-does not have PCS like VPP4D

## Slide 3: Catalyst Discharge Development
Velocys Pilot Plant Reactor 4D (VPP4D) Overview
Velocys Pilot Plant Reactor 4D (VPP4D):
-2 process layers (total of 6 waveforms)
-Core contained within pressure containment shell (PCS) pressurized with nitrogen
-approximate weight w/o headers is 3200lb
-process headers will be removed post operation prior to catalyst discharge
-catalyst retention materials will be removed prior to catalyst discharge
*Stand shown in drawings will be replaced with stand shown on next slide.
Ref. Drawing #: 1005875

## Slide 4: Catalyst Discharge Development
VPP4D stand
Reactor stand for catalyst discharge development:
-Allows for ~24 inches of clearance under the reactor to access entire process outlet face
-can be put on angle iron ‘track’ or positioned freely on floor.

## Slide 5: Catalyst Discharge Development
VPP4D- Top down view of process inlet face
Coolant Outlet

*process inlet and outlet headers are mirror images of one another (same dimensions)
Coolant Inlet 
2 layers
(3 waveforms each)
Thermocouple Access Port
Thermocouple Access Port
PCS pressure fill port
PCS pressure drain port
Ref. Drawing #: 1005873

## Slide 6: Catalyst Discharge Development
VPP4D Cross section of coolant system
Coolant Outlet
(Vapor) 
Coolant Inlet 
Coolant Outlet
(Condensate) 
Coolant Inlet header
Coolant Outlet header
Process Inlet
Process Outlet
Coolant Purge
Coolant Drain
Ref. Drawing #: 1005873

## Slide 7: Catalyst Discharge Development
VPP4D- Cross section of Process Layers
Process Inlet 
 Process Outlet
Thermocouple sheaths and access port
Thermocouple sheaths and access port
Process Layers (2 layers, 6 waveforms)
Ref. Drawing #: 1005873

## Slide 8: Catalyst Discharge Development
VPP4D – Process Header (detail A)
Top down view of process header
*Dimensions clear in PDF of drawings
Process headers taper from ~6.7 inches to ~1.7inches at the process face.
Ref. Drawing #: 1005873

## Slide 9: Catalyst Discharge Development
Top down view of process channels (detail B)
Copper waveforms are ~6.5 inches by ~0.25 inches and extend ~24 inches through reactor.
Ref. Drawing #: 1005873

## Slide 10: Catalyst Discharge Development
VPP2 Top down view of process inlet
Additional support added to reactor post fabrication (not shown in drawings)
Additional support added to reactor post fabrication (not shown in drawings)
Coolant Inlet 
Coolant Outlet

Process Inlet
Ref. Drawing #: 1002984

## Slide 11: Catalyst Discharge Development
VPP2- Cross Section of Coolant
Coolant Outlet
(Vapor) 
Coolant Inlet 
Coolant Outlet
(Condensate) 
Coolant Inlet header
Coolant Outlet header
Process Inlet
Process Outlet
Ref. Drawing #: 1002984

## Slide 12: Catalyst Discharge Development
VPP2- Cross Section of Process Layers
Process Inlet 
 Process Outlet
Process Layers (2 layers, 6 waveforms)
Additional supports (not shown in drawings)
Additional supports (not shown in drawings)
Ref. Drawing #: 1002984

## Slide 13: Catalyst Discharge Development
VPP2 cross section of process header
Ref. Drawing #: 1002984