## LONG TUBE REACTOR

MP Interconsulting

Issued date: August 30, 2002.

1. Specification

Model: Tubular transducer (S/N: M12-0208-095)

Total reactor-tube length: 1500 mm.

Active tube length: 1200 mm

Tube external diameter: 48.4mm

Tube internal diameter: 42.3mm

Material: 316L

Number of transducers: 24 pcs

Transducers: Silicone protected against water and humidity.

Frequency: 40 KHz

Power: 1200W – 1500W, continuous

2. Test conditions

MMM-sweeping generator, on 1200W until 1500 W

Temperature: 25°C

Aluminum foil: Placed inside disintegrated in 5 seconds

3. Impedance Characteristic

See attached file

4. Pictures

See attached file