#### Option 1:    MMM Tube Transducer

- This submersible transducer array is constructed of stainless steel with a Hard-Cr plating.

- When driven by an MMM generator its unique construction and shape stimulate a full range of wideband harmonic frequencies and ultrasonic effects in liquid.

- Strong even cavitation along the entire tube length.

- MMM technology eliminates standing waves to improve cleaning and sonochemical reaction.

- Available in 600 W, 900 W, 1200 W, 1500 W, and higher on custom order.

- The Flexible Hose version allows the Tube Transducer to be submersed in any tank configuration, in any position (vertical, horizontal, diagonal), and may be easily moved form tank to tank.

- The Through Tank Wall version allows for secure and fixed mounting to a tank wall or base in any position (vertical, horizontal, diagonal).

| Flexible Hose Connection | Through Tank Wall Connection |
| --- | --- |

| MODEL | TU-28-600 | TU-28-900 | TU-28-1200 | TU-28-1500 |
| --- | --- | --- | --- | --- |
| Power | 600 watt | 900 watt | 1200 watt | 1500 watt |
| Frequency | 28 Khz | 28 Khz | 28 Khz | 28 Khz |
| Dimension | Ø 76.3 x L 310 mm | Ø 76.3 x L 460 mm | Ø 76.3 x L 580 mm | Ø 76.3 x L 680 mm |

Option 1:    MMM Tube Transducer Possible Applications

| Option 1A: Ultrasonic Bath with MMM Tube Transducer | Option 1B: Flow-Thru Chamber with MMM Tube Transducer |
| --- | --- |

#### Option 2:    High Power Fixed Frequency Piston Probe

- 20 kHz Fixed frequency

- 2,000 watts max

- Booster Ratio 1:2.0

- Fullwave Probe (titanium)

  - Diameter = 50mm

  - Length = 250 mm

- Very high Axial energy produces strong cavitation and acoustic power for mixing, homogenization, flock & particle breakdown.

- New probe design also provides high radial energy for strong cavitation along the probe length.

| Power Draw Test: In Water |
| --- |
| Probe Submerged | 50% Amplitude | 100% Amplitude |
| Full submerge: | 1,000 W | 1,500 W |
| ½ Submerge: | 600 W | 1,000 W |
| ½ Submerge: | 600 W | 1,000 W |
| ¼ Submerge: | 300 W | 600 W |