WELDING SONICATOR GENERATOR

Protocol Description

RS485 ModBus RTU

# CONTENTS

CONTENTS	2

25-pin DSUB I/O  socket	3

Interface socket  RS485 ModBus - RJ 45 CONNECTOR:	4

Bus Description	5

CRC Generation	6

Registers Definition	6

The generator supports standard RS485 ModBus RTU protocol.  RS485 Bus is available by 25-pin DSUB I/O  socket on the back side panel and through RJ45 connector on the front panel of the generator.

# 15-pin DSUB I/O  socket

## Assignment of the 15-pin DSUB interface socket

| PIN No. on DSUB SOCKET Interface X1 | Signal name | Description |
| --- | --- | --- |
| 1 | +12 VOLT OUT | 15 Volt for external use |
| 2 | POUT | Output 0 – 10 Volt = Power output 0 – 100 % |
| 3 | P-EXT.-IN | Input 0 – 10 Volt for power control |
| 4 | GND | Internal Ground for analog input and output internal (GND) |
| 5/9 | HF-DA-ERROR | Common sigmal for HF-DA-ERROR |
| 6 | HF-DA | Optocoupler output “HF-DA” |
| 7 | ERROR | Optocoupler output “ERROR” |
| 8 | A | ModBus over RS485 “A” signal |
| 9/5 | HF-DA-ERROR | Relay root (shared) for “HF-DA” and “ERROR” |
| 10 | B | ModBus over RS485 ”B” sigmal |
| 11 | Not connected |  |
| 12 | Not connected |  |
| 13 | FS-24 V | Remote START/STOP control input (with 10 – 24 Volt) |
| 14 | GND | internal (GND) |
| 15 | GND | internal (GND) |

# Interface socket  RS485 ModBus - RJ 45 CONNECTOR:

| PINS | DESCRIPTION |
| --- | --- |
| 1 | GND |
| 2 | GND |
| 3 | N/C |
| 4 | A |
| 5 | B |
| 6 | N/C |
| 7 | 12 V DC |
| 8 | 12 V DC |

# Bus Description

• bus address of the device (1 - 255) –selecting via LCD panel

• transmission speed – 57 600 bps

• No parity check

• The number of Data-Bits is  RTU 8 Data-Bits

• The number of STOP-Bits is  1 STOP-Bit

Important remarks for operation in the Master/Slave-System:

!! The bus address must be differently adjusted for each device

!! Transmission mode, baud rate and parity must be identical

All data in a MODBUS-Slave are allocated to addresses. Data access (read or write) is made by the

corresponding control command and the indication of the corresponding data address.

In general, a MODBUS telegram starts with the address of the slave, followed by a control

command (e.g. read register) and the data. By means of the checksum at the telegram end, the bus

participants can recognize transmission errors.

The following MODBUS – control commands are supported:

| Description | Function code |
| --- | --- |
| Read Registers | 0x03 |
| Write Registers | 0x10 |

Example:

Read Registers 3 (0x03)

Query

| Field Name | Example |
| --- | --- |
| Slave Address | 0x11 |
| Function | 0x03 |
| Starting Address Hi | 0x00 |
| Starting Address Lo | 0x6B |
| No. of Points Hi | 0x00 |
| No. of Points Lo | 0x03 |
| Error Check ( CRC) | –– |

Response

| Field Name | Example |
| --- | --- |
| Slave Address | 0x11 |
| Function | 0x03 |
| Byte Count | 0x06 |
| Data Hi | 0x02 |
| Data Lo | 0x2B |
| Data Hi | 0x00 |
| Data Lo | 0x00 |
| Data Hi | 0x00 |
| Data Lo | 0x64 |
| Error Check ( CRC) | –– |

Write Registers  16 (0x10)

Query

| Field Name | Example |
| --- | --- |
| Slave Address | 0x11 |
| Function | 0x10 |
| Starting Address Hi | 0x00 |
| Starting Address Lo | 0x01 |
| No. of Registers Hi | 0x00 |
| No. of Registers Lo | 0x02 |
| Byte Count | 0x04 |
| Data Hi | 0x00 |
| Data Lo | 0x0A |
| Data Hi | 0x01 |
| Data Lo | 0x02 |
| Error Check (CRC) | –– |

Response

| Field Name | Example |
| --- | --- |
| Slave Address | 11 |
| Function | 10 |
| Starting Address Hi | 00 |
| Starting Address Lo | 01 |
| No. of Registers Hi | 00 |
| No. of Registers Lo | 02 |
| Error Check (CRC) | –– |

# CRC Generation

A procedure for generating a CRC is:

1, Load a 16–bit register with FFFF hex (all 1’s). Call this the CRC register.

2. Exclusive OR the first 8–bit byte of the message with the low–order byte

of the 16–bit CRC register, putting the result in the CRC register.

3. Shift the CRC register one bit to the right (toward the LSB), zero–filling the

MSB. Extract and examine the LSB.

4. (If the LSB was 0): Repeat Step 3 (another shift).

(If the LSB was 1): Exclusive OR the CRC register with the polynomial

value A001 hex (1010 0000 0000 0001).

5. Repeat Steps 3 and 4 until 8 shifts have been performed. When this is

done, a complete 8–bit byte will have been processed

When the 16–bit CRC (two 8–bit bytes) is transmitted in the message, the

low-order byte will be transmitted first, followed by the high-order byte.

# Registers Definition

| MODBUS RS485 RTU no parity, 8 bit data, 1 stop bit |
| --- |
| register# | address | action | parameter | dim/resolution | type | format |
| 0 | 0x0000 | R/W | spare | ru | unsigned INT |  |
| 1 | 0x0001 | R | Phase | ru | unsigned INT |  |
| 2 | 0x0002 | R | Frequency | 0.001 kHz | fixed point | XX.XX kHz |
| 3 | 0x0003 | R | Temperature | °C | unsigned INT | XX °C |
| 4 | 0x0004 | R | Amplitude | 0.10% | fixed point | XXX.X % |
| 5 | 0x0005 | R | AV | % | fixed point | XXX.X % |
| 6 | 0x0006 | R | AV PWM | % | fixed point | XXX.X % |
| 7 | 0x0007 | R | Power | W | unsigned INT |  |
| 8 | 0x0008 | R | Output Current | 0.005 A | fixed point | X.XXX A |
| 9 | 0x0009 | R | Last peak power | W | unsigned INT |  |
| 10 | 0x000A | R | Last energy | Ws | unsigned INT |  |
| 11 | 0x000B | R | Last time | 0,01 s | fixed point | X.XX s |
| 12 | 0x000C | R | Sonicator Time | 1 s | unsigned INT |  |
| 13 | 0x000D | R | Sonicator Time ON | 1 s | unsigned INT |  |
| 14 | 0x000E | R | Sonicator Time OFF | 1 s | unsigned INT |  |
| 15 | 0x000F | R | Sonicator Energy High | J | long INT high part |  |
| 16 | 0x0010 | R | Sonicator Energy Low | J | long INT low part |  |
| 17 | 0x0011 | R | Status | ASCII code | unsigned BYTE | 0x30 STOP |
|  |  |  |  |  |  | 0x31 START |
|  |  |  |  |  |  | 0x32 Over Current |
|  |  |  |  |  |  | 0x33 Over Heat |
|  |  |  |  |  |  | 0x34 Over Voltage |
|  |  |  |  |  |  | 0x35 Limit Time |
|  |  |  |  |  |  | 0x36 Limit Power |
|  |  |  |  |  |  | 0x37 Limit Energy |
|  |  |  |  |  |  | 0x38 Untested |
|  |  |  |  |  |  | 0x39 Over Load |
|  |  |  |  |  |  | 0x3A HF Over Current |
|  |  |  |  |  |  | 0x3B External Overheat |
| 18 | 0x0012 | R/W | spare | ru | unsigned INT |  |
| 19 | 0x0013 | R/W | spare | ru | unsigned INT |  |
| 20 | 0x0014 | R/W | spare | ru | unsigned INT |  |
| 21 | 0x0015 | R/W | spare | ru | unsigned INT |  |
| 22 | 0x0016 | R/W | spare | ru | unsigned INT |  |
| 23 | 0x0017 | R/W | spare | ru | unsigned INT |  |
|  |  | R/W | spare | ru | unsigned INT |  |
|  |  | R/W | spare | ru | unsigned INT |  |
| 24 | 0x0018 | R/W | spare | ru | unsigned INT |  |
| 25 | 0x0019 | R/W | spare | ru | unsigned INT |  |
| 26 | 0x001A | R/W | spare | ru | unsigned INT |  |
| 27 | 0x001B | R/W | spare | ru | unsigned INT |  |
| 28 | 0x001C | R/W | spare | ru | unsigned INT |  |
| 29 | 0x001D | W | Command Word | bit field | usigned BYTE | bit 0 - START |
|  |  |  |  |  |  | bit 1 - STOP |
|  |  |  |  |  |  | bit 2 - SCAN |
|  |  |  |  |  |  | bit 3 - WRITE |
|  |  |  |  |  |  | bit 4 - TUNE |
| 30 | 0x001E | R/W | Phase | ru | usigned INT |  |
| 31 | 0x001F | R/W | Start frequency set point | 0,001 kHz | fixed point | XX.XXX kHz |
| 32 | 0x0020 | R/W | Span | 0,001 kHz | fixed point | X.XXX kHz |
| 33 | 0x0021 | R/W | Amplitude Set Point | 0.10% | fixed point | XXX.X % |
| 34 | 0x0022 | R/W | Scanning Range | 0,001 kHz | fixed point | X.XXX kHz |
| 35 | 0x0023 | R/W | Startup mode | ru | unsigned INT | 0-Normal without Scan |
|  |  |  |  |  |  | 1 - Scanning only on Safe Start |
|  |  |  |  |  |  | 2 - Scanning every time |
|  |  |  |  |  |  | 3 - Hot Start |
| 36 | 0x0024 | R/W | Current Set Point | 0.005 A | fixed point | X.XXX A |
| 37 | 0x0025 | R/W | spare | ru | unsigned INT |  |
| 38 | 0x0026 | R/W | Mode | ru | unsigned INT | 0 - Welding |
|  |  |  |  |  |  | 1 - Sonicator |
| 39 | 0x0027 | R/W | Sampling Time | s | unsigned INT |  |
| 40 | 0x0028 | R/W | spare | ru | unsigned INT |  |
| 41 | 0x0029 | R/W | spare | ru | unsigned INT |  |
| 42 | 0x002A | R/W | spare | ru | unsigned INT |  |
| 43 | 0x002B | R/W | spare | ru | unsigned INT |  |
| 44 | 0x002C | R/W | spare | ru | unsigned INT |  |
| 45 | 0x002D | R/W | spare | ru | unsigned INT |  |
| 46 | 0x002E | R/W | spare | ru | unsigned INT |  |
| 47 | 0x002F | R/W | spare | ru | unsigned INT |  |
| 48 | 0x0030 | R/W | spare | ru | unsigned INT |  |
| 49 | 0x0031 | R/W | spare | ru | unsigned INT |  |
| 50 | 0x0032 | R/W | Peak Power | W | unsigned INT |  |
| 51 | 0x0033 | R/W | Energy | Ws | unsigned INT |  |
| 52 | 0x0034 | R/W | Time | 0.01s | fixed point | X.XX s |
| 53 | 0x0035 | R/W | Peak Power Plus | 1W | unsigned INT |  |
| 54 | 0x0036 | R/W | Peak Power Minus | 1W | unsigned INT |  |
| 55 | 0x0037 | R/W | Energy Plus | 1W | unsigned INT |  |
| 56 | 0x0038 | R/W | Energy Minus | 1W | unsigned INT |  |
| 57 | 0x0039 | R/W | Time Plus | 0.01s | fixed point | X.XX s |
| 58 | 0x003A | R/W | Time Minus | 0.01s | fixed point | X.XX s |
| 59 | 0x003B | R/W | Amplitude Regulator | 10 ru | unsigned INT |  |
| 60 | 0x003C | R/W | Phase Regulator | 10 ru | unsigned INT |  |
| 61 | 0x003D | R/W | StartUp Regulator | 10 ru | unsigned INT |  |
| 62 | 0x003E | R/W | Power Offset | 1W | unsigned INT |  |
| 63 | 0x003F | R/W | Power Scale | 0.01 ru | fixed point | X.XX |
| 64 | 0x0040 | R/W | Amplitude Scale | 0.01 ru | fixed point | X.XX |
| 65 | 0x0041 | R/W | bit field | bit field | unsigned BYTE | bit 0 - Overload Protection Trip |
|  |  |  |  |  |  | bit 1 - Overload Protection Warning |
|  |  |  |  |  |  | bit 2 - Test Button Push |
|  |  |  |  |  |  | bit 3 - Test Button Letch |
|  |  |  |  |  |  | bit 4 - Analog Input Amplitude SetPoint |
|  |  |  |  |  |  | bit 5 - Analog Input Transducer Temperature |
| 66 | 0x0042 | R/W | Amplitude Ramp | ru | unsigned INT |  |
| 67 | 0x0043 | R/W | spare | ru | unsigned INT |  |
| 68 | 0x0044 | R/W | spare | ru | unsigned INT |  |
| 69 | 0x0045 | R/W | spare | ru | unsigned INT |  |
| 70 | 0x0046 | R/W | Process Time High | s | long INT high part |  |
| 71 | 0x0047 | R/W | Process Time Low | s | long INT low part |  |
| 72 | 0x0048 | R/W | Time OFF | s | unsigned INT |  |
| 73 | 0x0049 | R/W | Time ON | s | unsigned INT |  |
| 74 | 0x004A | R/W | Process Energy High | J | long INT high part |  |
| 75 | 0x004B | R/W | Process Energy Low | J | long INT low part |  |
| 76 | 0x004C | R/W | Input Voltage | ru | unsigned INT | 1 - low |
|  |  |  |  |  |  | 2 - middle |
|  |  |  |  |  |  | 3 - high |
| 77 | 0x004D | R/W | Output Choke | uh | unsigned INT |  |
| 78 | 0x004E | R/W | Output Capacitor | nF | unsigned INT |  |
| 79 | 0x004F | R/W | Extra Span | 0.001 kHz | fixed point | X.XXX kHz |
| 80 | 0x0050 | R/W | PWM | % | unsigned INT |  |
| 81 | 0x0051 | R/W | Sweeping | 0.001 kHz | fixed point | X.XXX kHz |
| 82 | 0x0052 | R/W | Sweeping Frequency | 0.1 Hz | fixed point | X.X Hz |
| 83 | 0x0053 | R/W | Smoothing | 0.01 ru | fixed point | X.XX |
| 84 | 0x0054 | R/W | FSWM Frequency | 1 Hz | unsigned INT |  |
| 85 | 0x0055 | R/W | FSWM Period | ru | unsigned INT |  |
| 86 | 0x0056 | R/W | FSWM Ratio | % | unsigned INT |  |
| 87 | 0x0057 | R/W | Mode Sweep | ru | unsigned INT | 0 - continuous |
|  |  |  |  |  |  | 1 - AMMM |
|  |  |  |  |  |  | 2 - Periodic |
| ………. |  |  |  |  |  |  |
| 500-699 | 0x01F4 - 0x02BB | R | Scanning DATA |  |  |  |
| ………. |  |  |  |  |  |  |